## Slide 1: Branching Structures and Algorithm conversion to assembly language
Course Code: COE 3205
Dept. of Computer Science
Faculty of Science and Technology
Lab No: | 7 | Week No: | 8 | Semester: | Fall 22-23
Lecturer: |  |  |  |  | 
Course Title: Computer Organization & Architecture

## Slide 2: Lab Outline
Branching structures enable a program to take different paths, depending on conditions.
Here, We will look at three structures.
      IF-THEN
      IF-THEN-ELSE
      CASE
Algorithm conversion to assembly language

## Slide 3: IF-THEN
IF condition is true.
THEN
execute true-branch statements
END_IF

## Slide 4: A Pseudo Code , Algorithm and Code for IF-THEN
The condition is an expression that is either true or false.
lf It is true, the true-branch statements are executed.
lf It is false, nothing is done, and the program goes on to whatever follows.
Example: to Replace a number in AX by its absolute value…
IF AX < 0
THEN
replace AX by -AX
END_IF
CMP AX, 0
JNL END_IF
NEG AX
END_IF:

## Slide 5: IF-THEN-ELSE
IF condition is true
THEN
execute true-branch statements
ELSE
execute false-branch statements
END_IF

## Slide 6: IF-THEN-ELSE
Example: Suppose AL and BL contain extended ASCII characters. Display the one that comes
IF AL <= BL
THEN
Display the character in AL
ELSE
Display the character in BL
END IF
MOV AH,2
CMP AL,BL ;AL<=BL ?
JNBE ELSE_
MOV DL,AL
JMP DISPLAY
ELSE_:
MOV DL,BL
DISPLAY:
INT 2lh

## Slide 7: CASE
A CASE is a multi-way branch structure that tests a register, variable, or expression for particular values or a range of values.
CASE Expression
Values_1: Statement_1
Values_2: Statement_2
…
Values_n: Statement_n
END_CASE

## Slide 8: CASE
Example: If AX contains a negative number, put -1 in BX; if AX contains 0, put 0 in BX; and if AX contains a positive number, put 1 in BX.
CASE AX
  <0 : put -1 in BX
  =0 : put 0 in BX
  >0 : put +l in BX
END_CASE
CMP AX,O
JL NEGATIVE
JE ZERO
JG POSITIVE
NEGATIVE:
MOV BX,-1
JMP END_CASE
ZERO:
MOV BX,0
JMP END_CASE
POSITIVE:
MOV BX, l
END_CASE:

## Slide 9: Lab Tasks
Task: 1
Write a program to convert following code into assembly program.
      IF AX < 0
      THEN
      PUT -1 IN BX
      END IF

## Slide 10: Lab Tasks
Task: 2
Write a program to convert following code into assembly progam.
        IF "AL < 0
        THEN
        put FFh in AH'
        ELSE
        put 0 in AH
        END_IF

## Slide 11: Lab Tasks
Task: 3
Write a program to convert following code into assembly program.

## Slide 12: Lab Tasks
Task: 4
Write a program to convert following code into assembly program.

## Slide 13: Lab Tasks
Task: 5
Write a program to convert following code into assembly program.

## Slide 14: Lab Tasks
Task: 6
Write a program to convert following code into assembly program.

## Slide 15: Lab Tasks
Task: 7
Write a program to display "o" if AL contains 1 or 3; if AL contains 2 or 4, display "e"..

## Slide 16
Books
Assembly Language Programing and Organization of the IBM PC; by Ytha Yu, Charles Marut

## Slide 17
References
Assembly Language Programing and Organization of the IBM PC; by Ytha Yu, Charles Marut